        |INVITE from TU
        Timer A fires |INVITE sent
        Reset A, V Timer B fires
        INVITE sent +-----------+ or Transport Err.
        +---------| |---------------+inform TU
        | | Calling | |
        +-------->| |-------------->|
        +-----------+ 2xx |
        | | 2xx to TU |
        | |1xx |
    300-699 +---------------+ |1xx to TU |
   ACK sent | | |
resp. to TU | 1xx V |
        | 1xx to TU -----------+ |
        | +---------| | |
        | | |Proceeding |-------------->|
        | +-------->| | 2xx |
        | +-----------+ 2xx to TU |
        | 300-699 | |
        | ACK sent, | |
        | resp. to TU| |
        | | | NOTE:
        | 300-699 V |
        | ACK sent +-----------+Transport Err. | transitions
        | +---------| |Inform TU | labeled with
        | | | Completed |-------------->| the event
        | +-------->| | | over the action
        | +-----------+ | to take
        | ^ | |
        | | | Timer D fires |
        +--------------+ | - |
        | |
        V |
        +-----------+ |
        | | |
        | Terminated|<--------------+
        | |
        +-----------+

        Figure 5: INVITE client transaction

        |Request from TU
        |send request
        Timer E V
        send request +-----------+
        +---------| |-------------------+
        | | Trying | Timer F |
        +-------->| | or Transport Err.|
        +-----------+ inform TU |
        200-699 | | |
        resp. to TU | |1xx |
        +---------------+ |resp. to TU |
        | | |
        | Timer E V Timer F |
        | send req +-----------+ or Transport Err. |
        | +---------| | inform TU |
        | | |Proceeding |------------------>|
        | +-------->| |-----+ |
        | +-----------+ |1xx |
        | | ^ |resp to TU |
        | 200-699 | +--------+ |
        | resp. to TU | |
        | | |
        | V |
        | +-----------+ |
        | | | |
        | | Completed | |
        | | | |
        | +-----------+ |
        | ^ | |
        | | | Timer K |
        +--------------+ | - |
        | |
        V |
        NOTE: +-----------+ |
        | | |
        transitions | Terminated|<------------------+
        labeled with | |
        the event +-----------+
        over the action
        to take

        Figure 6: non-INVITE client transaction

        |INVITE
        |pass INV to TU
        INVITE V send 100 if TU won't in 200ms
        send response+-----------+
        +--------| |--------+101-199 from TU
        | | Proceeding| |send response
        +------->| |<-------+
        | | Transport Err.
        | | Inform TU
        | |--------------->+
        +-----------+ |
        300-699 from TU | |2xx from TU |
        send response | |send response |
        | +------------------>+
        | |
        INVITE V Timer G fires |
        send response+-----------+ send response |
        +--------| |--------+ |
        | | Completed | | |
        +------->| |<-------+ |
        +-----------+ |
        | | |
        ACK | | |
        - | +------------------>+
        | Timer H fires |
        V or Transport Err.|
        +-----------+ Inform TU |
        | | |
        | Confirmed | |
        | | |
        +-----------+ |
        | |
        |Timer I fires |
        |- |
        | |
        V |
        +-----------+ |
        | | |
        | Terminated|<---------------+
        | |
        +-----------+

        Figure 7: INVITE server transaction

        |Request received
        |pass to TU
        V
        +-----------+
        | |
        | Trying |-------------+
        | | |
        +-----------+ |200-699 from TU
        | |send response
        |1xx from TU |
        |send response |
        | |
        Request V 1xx from TU |
        send response+-----------+send response|
        +--------| |--------+ |
        | | Proceeding| | |
        +------->| |<-------+ |
        +<--------------| | |
        |Trnsprt Err +-----------+ |
        |Inform TU | |
        | | |
        | |200-699 from TU |
        | |send response |
        | Request V |
        | send response+-----------+ |
        | +--------| | |
        | | | Completed |<------------+
        | +------->| |
        +<--------------| |
        |Trnsprt Err +-----------+
        |Inform TU |
        | |Timer J fires
        | |-
        | |
        | V
        | +-----------+
        | | |
        +-------------->| Terminated|
        | |
        +-----------+

        Figure 8: non-INVITE server transaction

        +----------+ +----------+
        | | 1xx-notag | |
        | |----------->| |
        | Trying | |Proceeding|-----+
        | |---+ +-----| | |
        | | | | | | |
        +----------+ | | +----------+ |
        | | | | | |
        | | | | | |
        +<--C-----C--+ |1xx-tag |
        | | | | |
        cancelled| | | V |
        rejected| | |1xx-tag +----------+ |
        | | +------->| | |2xx
        | | | | |
        +<--C--------------| Early |-----C---+ 1xx-tag
        | | replaced | | | | w/new tag
        | | | |<----C---+ (new FSM
        | | +----------+ | instance
        | | 2xx | | created)
        | +----------------+ | |
        | | |2xx |
        | | | |
        V V V |
        +----------+ +----------+ |
        | | | | |
        | | | | |
        |Terminated|<-----------| Confirmed|<----+
        | | error | |
        | | timeout | |
        +----------+ replaced +----------+
        local-bye | ^
        remote-bye | |
        | |
        +------+
        2xx w. new tag
        (new FSM instance
        created)

        Figure 3

   The FSM for dialog state is shown in Figure 3.

17 Transactions

   SIP is a transactional protocol: interactions between components take
   place in a series of independent message exchanges. Specifically, a
   SIP transaction consists of a single request and any responses to
   that request, which include zero or more provisional responses and
   one or more final responses. In the case of a transaction where the
   request was an INVITE (known as an INVITE transaction), the
   transaction also includes the ACK only if the final response was not
   a 2xx response. If the response was a 2xx, the ACK is not considered
   part of the transaction.

      The reason for this separation is rooted in the importance of
      delivering all 200 (OK) responses to an INVITE to the UAC. To
      deliver them all to the UAC, the UAS alone takes responsibility

Rosenberg, et. al. Standards Track [Page 122]

RFC 3261 SIP: Session Initiation Protocol June 2002

      for retransmitting them (see Section 13.3.1.4), and the UAC alone
      takes responsibility for acknowledging them with ACK (see Section
      13.2.2.4). Since this ACK is retransmitted only by the UAC, it is
      effectively considered its own transaction.

   Transactions have a client side and a server side. The client side
   is known as a client transaction and the server side as a server
   transaction. The client transaction sends the request, and the
   server transaction sends the response. The client and server
   transactions are logical functions that are embedded in any number of
   elements. Specifically, they exist within user agents and stateful
   proxy servers. Consider the example in Section 4. In this example,
   the UAC executes the client transaction, and its outbound proxy
   executes the server transaction. The outbound proxy also executes a
   client transaction, which sends the request to a server transaction
   in the inbound proxy. That proxy also executes a client transaction,
   which in turn sends the request to a server transaction in the UAS.
   This is shown in Figure 4.

   +---------+ +---------+ +---------+ +---------+
   | +-+|Request |+-+ +-+|Request |+-+ +-+|Request |+-+ |
   | |C||------->||S| |C||------->||S| |C||------->||S| |
   | |l|| ||e| |l|| ||e| |l|| ||e| |
   | |i|| ||r| |i|| ||r| |i|| ||r| |
   | |e|| ||v| |e|| ||v| |e|| ||v| |
   | |n|| ||e| |n|| ||e| |n|| ||e| |
   | |t|| ||r| |t|| ||r| |t|| ||r| |
   | | || || | | || || | | || || | |
   | |T|| ||T| |T|| ||T| |T|| ||T| |
   | |r|| ||r| |r|| ||r| |r|| ||r| |
   | |a|| ||a| |a|| ||a| |a|| ||a| |
   | |n|| ||n| |n|| ||n| |n|| ||n| |
   | |s||Response||s| |s||Response||s| |s||Response||s| |
   | +-+|<-------|+-+ +-+|<-------|+-+ +-+|<-------|+-+ |
   +---------+ +---------+ +---------+ +---------+
      UAC Outbound Inbound UAS
        Proxy Proxy

        Figure 4: Transaction relationships

   A stateless proxy does not contain a client or server transaction.
   The transaction exists between the UA or stateful proxy on one side,
   and the UA or stateful proxy on the other side. As far as SIP
   transactions are concerned, stateless proxies are effectively
   transparent. The purpose of the client transaction is to receive a
   request from the element in which the client is embedded (call this
   element the "Transaction User" or TU; it can be a UA or a stateful
   proxy), and reliably deliver the request to a server transaction.

Rosenberg, et. al. Standards Track [Page 123]

RFC 3261 SIP: Session Initiation Protocol June 2002

   The client transaction is also responsible for receiving responses
   and delivering them to the TU, filtering out any response
   retransmissions or disallowed responses (such as a response to ACK).
   Additionally, in the case of an INVITE request, the client
   transaction is responsible for generating the ACK request for any
   final response accepting a 2xx response.

   Similarly, the purpose of the server transaction is to receive
   requests from the transport layer and deliver them to the TU. The
   server transaction filters any request retransmissions from the
   network. The server transaction accepts responses from the TU and
   delivers them to the transport layer for transmission over the
   network. In the case of an INVITE transaction, it absorbs the ACK
   request for any final response excepting a 2xx response.

   The 2xx response and its ACK receive special treatment. This
   response is retransmitted only by a UAS, and its ACK generated only
   by the UAC. This end-to-end treatment is needed so that a caller
   knows the entire set of users that have accepted the call. Because
   of this special handling, retransmissions of the 2xx response are
   handled by the UA core, not the transaction layer. Similarly,
   generation of the ACK for the 2xx is handled by the UA core. Each
   proxy along the path merely forwards each 2xx response to INVITE and
   its corresponding ACK.

17.1 Client Transaction

   The client transaction provides its functionality through the
   maintenance of a state machine.

   The TU communicates with the client transaction through a simple
   interface. When the TU wishes to initiate a new transaction, it
   creates a client transaction and passes it the SIP request to send
   and an IP address, port, and transport to which to send it. The
   client transaction begins execution of its state machine. Valid
   responses are passed up to the TU from the client transaction.

   There are two types of client transaction state machines, depending
   on the method of the request passed by the TU. One handles client
   transactions for INVITE requests. This type of machine is referred
   to as an INVITE client transaction. Another type handles client
   transactions for all requests except INVITE and ACK. This is
   referred to as a non-INVITE client transaction. There is no client
   transaction for ACK. If the TU wishes to send an ACK, it passes one
   directly to the transport layer for transmission.

Rosenberg, et. al. Standards Track [Page 124]

RFC 3261 SIP: Session Initiation Protocol June 2002

   The INVITE transaction is different from those of other methods
   because of its extended duration. Normally, human input is required
   in order to respond to an INVITE. The long delays expected for
   sending a response argue for a three-way handshake. On the other
   hand, requests of other methods are expected to complete rapidly.
   Because of the non-INVITE transaction's reliance on a two-way
   handshake, TUs SHOULD respond immediately to non-INVITE requests.

17.1.1 INVITE Client Transaction

17.1.1.1 Overview of INVITE Transaction

   The INVITE transaction consists of a three-way handshake. The client
   transaction sends an INVITE, the server transaction sends responses,
   and the client transaction sends an ACK. For unreliable transports
   (such as UDP), the client transaction retransmits requests at an
   interval that starts at T1 seconds and doubles after every
   retransmission. T1 is an estimate of the round-trip time (RTT), and
   it defaults to 500 ms. Nearly all of the transaction timers
   described here scale with T1, and changing T1 adjusts their values.
   The request is not retransmitted over reliable transports. After
   receiving a 1xx response, any retransmissions cease altogether, and
   the client waits for further responses. The server transaction can
   send additional 1xx responses, which are not transmitted reliably by
   the server transaction. Eventually, the server transaction decides
   to send a final response. For unreliable transports, that response
   is retransmitted periodically, and for reliable transports, it is
   sent once. For each final response that is received at the client
   transaction, the client transaction sends an ACK, the purpose of
   which is to quench retransmissions of the response.

17.1.1.2 Formal Description

   The state machine for the INVITE client transaction is shown in
   Figure 5. The initial state, "calling", MUST be entered when the TU
   initiates a new client transaction with an INVITE request. The
   client transaction MUST pass the request to the transport layer for
   transmission (see Section 18). If an unreliable transport is being
   used, the client transaction MUST start timer A with a value of T1.
   If a reliable transport is being used, the client transaction SHOULD
   NOT start timer A (Timer A controls request retransmissions). For
   any transport, the client transaction MUST start timer B with a value
   of 64*T1 seconds (Timer B controls transaction timeouts).

   When timer A fires, the client transaction MUST retransmit the
   request by passing it to the transport layer, and MUST reset the
   timer with a value of 2*T1. The formal definition of retransmit
Rosenberg, et. al. Standards Track [Page 125]

RFC 3261 SIP: Session Initiation Protocol June 2002

   within the context of the transaction layer is to take the message
   previously sent to the transport layer and pass it to the transport
   layer once more.

   When timer A fires 2*T1 seconds later, the request MUST be
   retransmitted again (assuming the client transaction is still in this
   state). This process MUST continue so that the request is
   retransmitted with intervals that double after each transmission.
   These retransmissions SHOULD only be done while the client
   transaction is in the "calling" state.

   The default value for T1 is 500 ms. T1 is an estimate of the RTT
   between the client and server transactions. Elements MAY (though it
   is NOT RECOMMENDED) use smaller values of T1 within closed, private
   networks that do not permit general Internet connection. T1 MAY be
   chosen larger, and this is RECOMMENDED if it is known in advance
   (such as on high latency access links) that the RTT is larger.
   Whatever the value of T1, the exponential backoffs on retransmissions
   described in this section MUST be used.

   If the client transaction is still in the "Calling" state when timer
   B fires, the client transaction SHOULD inform the TU that a timeout
   has occurred. The client transaction MUST NOT generate an ACK. The
   value of 64*T1 is equal to the amount of time required to send seven
   requests in the case of an unreliable transport.

   If the client transaction receives a provisional response while in
   the "Calling" state, it transitions to the "Proceeding" state. In the
   "Proceeding" state, the client transaction SHOULD NOT retransmit the
   request any longer. Furthermore, the provisional response MUST be
   passed to the TU. Any further provisional responses MUST be passed
   up to the TU while in the "Proceeding" state.

   When in either the "Calling" or "Proceeding" states, reception of a
   response with status code from 300-699 MUST cause the client
   transaction to transition to "Completed". The client transaction
   MUST pass the received response up to the TU, and the client
   transaction MUST generate an ACK request, even if the transport is
   reliable (guidelines for constructing the ACK from the response are
   given in Section 17.1.1.3) and then pass the ACK to the transport
   layer for transmission. The ACK MUST be sent to the same address,
   port, and transport to which the original request was sent. The
   client transaction SHOULD start timer D when it enters the
   "Completed" state, with a value of at least 32 seconds for unreliable
   transports, and a value of zero seconds for reliable transports.
   Timer D reflects the amount of time that the server transaction can
   remain in the "Completed" state when unreliable transports are used.
   This is equal to Timer H in the INVITE server transaction, whose

Rosenberg, et. al. Standards Track [Page 126]

RFC 3261 SIP: Session Initiation Protocol June 2002

   default is 64*T1. However, the client transaction does not know the
   value of T1 in use by the server transaction, so an absolute minimum
   of 32s is used instead of basing Timer D on T1.

   Any retransmissions of the final response that are received while in
   the "Completed" state MUST cause the ACK to be re-passed to the
   transport layer for retransmission, but the newly received response
   MUST NOT be passed up to the TU. A retransmission of the response is
   defined as any response which would match the same client transaction
   based on the rules of Section 17.1.3.

Rosenberg, et. al. Standards Track [Page 127]

RFC 3261 SIP: Session Initiation Protocol June 2002

        |INVITE from TU
        Timer A fires |INVITE sent
        Reset A, V Timer B fires
        INVITE sent +-----------+ or Transport Err.
        +---------| |---------------+inform TU
        | | Calling | |
        +-------->| |-------------->|
        +-----------+ 2xx |
        | | 2xx to TU |
        | |1xx |
    300-699 +---------------+ |1xx to TU |
   ACK sent | | |
resp. to TU | 1xx V |
        | 1xx to TU -----------+ |
        | +---------| | |
        | | |Proceeding |-------------->|
        | +-------->| | 2xx |
        | +-----------+ 2xx to TU |
        | 300-699 | |
        | ACK sent, | |
        | resp. to TU| |
        | | | NOTE:
        | 300-699 V |
        | ACK sent +-----------+Transport Err. | transitions
        | +---------| |Inform TU | labeled with
        | | | Completed |-------------->| the event
        | +-------->| | | over the action
        | +-----------+ | to take
        | ^ | |
        | | | Timer D fires |
        +--------------+ | - |
        | |
        V |
        +-----------+ |
        | | |
        | Terminated|<--------------+
        | |
        +-----------+

        Figure 5: INVITE client transaction

   If timer D fires while the client transaction is in the "Completed"
   state, the client transaction MUST move to the terminated state.

   When in either the "Calling" or "Proceeding" states, reception of a
   2xx response MUST cause the client transaction to enter the
   "Terminated" state, and the response MUST be passed up to the TU.
   The handling of this response depends on whether the TU is a proxy

Rosenberg, et. al. Standards Track [Page 128]

RFC 3261 SIP: Session Initiation Protocol June 2002

   core or a UAC core. A UAC core will handle generation of the ACK for
   this response, while a proxy core will always forward the 200 (OK)
   upstream. The differing treatment of 200 (OK) between proxy and UAC
   is the reason that handling of it does not take place in the
   transaction layer.

   The client transaction MUST be destroyed the instant it enters the
   "Terminated" state. This is actually necessary to guarantee correct
   operation. The reason is that 2xx responses to an INVITE are treated
   differently; each one is forwarded by proxies, and the ACK handling
   in a UAC is different. Thus, each 2xx needs to be passed to a proxy
   core (so that it can be forwarded) and to a UAC core (so it can be
   acknowledged). No transaction layer processing takes place.
   Whenever a response is received by the transport, if the transport
   layer finds no matching client transaction (using the rules of
   Section 17.1.3), the response is passed directly to the core. Since
   the matching client transaction is destroyed by the first 2xx,
   subsequent 2xx will find no match and therefore be passed to the
   core.

17.1.1.3 Construction of the ACK Request

   This section specifies the construction of ACK requests sent within
   the client transaction. A UAC core that generates an ACK for 2xx
   MUST instead follow the rules described in Section 13.

   The ACK request constructed by the client transaction MUST contain
   values for the Call-ID, From, and Request-URI that are equal to the
   values of those header fields in the request passed to the transport
   by the client transaction (call this the "original request"). The To
   header field in the ACK MUST equal the To header field in the
   response being acknowledged, and therefore will usually differ from
   the To header field in the original request by the addition of the
   tag parameter. The ACK MUST contain a single Via header field, and
   this MUST be equal to the top Via header field of the original
   request. The CSeq header field in the ACK MUST contain the same
   value for the sequence number as was present in the original request,
   but the method parameter MUST be equal to "ACK".

Rosenberg, et. al. Standards Track [Page 129]

RFC 3261 SIP: Session Initiation Protocol June 2002

   If the INVITE request whose response is being acknowledged had Route
   header fields, those header fields MUST appear in the ACK. This is
   to ensure that the ACK can be routed properly through any downstream
   stateless proxies.

   Although any request MAY contain a body, a body in an ACK is special
   since the request cannot be rejected if the body is not understood.
   Therefore, placement of bodies in ACK for non-2xx is NOT RECOMMENDED,
   but if done, the body types are restricted to any that appeared in
   the INVITE, assuming that the response to the INVITE was not 415. If
   it was, the body in the ACK MAY be any type listed in the Accept
   header field in the 415.

   For example, consider the following request:

   INVITE sip:bob@biloxi.com SIP/2.0
   Via: SIP/2.0/UDP pc33.atlanta.com;branch=z9hG4bKkjshdyff
   To: Bob <sip:bob@biloxi.com>
   From: Alice <sip:alice@atlanta.com>;tag=88sja8x
   Max-Forwards: 70
   Call-ID: 987asjd97y7atg
   CSeq: 986759 INVITE

   The ACK request for a non-2xx final response to this request would
   look like this:

   ACK sip:bob@biloxi.com SIP/2.0
   Via: SIP/2.0/UDP pc33.atlanta.com;branch=z9hG4bKkjshdyff
   To: Bob <sip:bob@biloxi.com>;tag=99sa0xk
   From: Alice <sip:alice@atlanta.com>;tag=88sja8x
   Max-Forwards: 70
   Call-ID: 987asjd97y7atg
   CSeq: 986759 ACK

17.1.2 Non-INVITE Client Transaction

17.1.2.1 Overview of the non-INVITE Transaction

   Non-INVITE transactions do not make use of ACK. They are simple
   request-response interactions. For unreliable transports, requests
   are retransmitted at an interval which starts at T1 and doubles until
   it hits T2. If a provisional response is received, retransmissions
   continue for unreliable transports, but at an interval of T2. The
   server transaction retransmits the last response it sent, which can
   be a provisional or final response, only when a retransmission of the
   request is received. This is why request retransmissions need to
   continue even after a provisional response; they are to ensure
   reliable delivery of the final response.

Rosenberg, et. al. Standards Track [Page 130]

RFC 3261 SIP: Session Initiation Protocol June 2002

   Unlike an INVITE transaction, a non-INVITE transaction has no special
   handling for the 2xx response. The result is that only a single 2xx
   response to a non-INVITE is ever delivered to a UAC.

17.1.2.2 Formal Description

   The state machine for the non-INVITE client transaction is shown in
   Figure 6. It is very similar to the state machine for INVITE.

   The "Trying" state is entered when the TU initiates a new client
   transaction with a request. When entering this state, the client
   transaction SHOULD set timer F to fire in 64*T1 seconds. The request
   MUST be passed to the transport layer for transmission. If an
   unreliable transport is in use, the client transaction MUST set timer
   E to fire in T1 seconds. If timer E fires while still in this state,
   the timer is reset, but this time with a value of MIN(2*T1, T2).
   When the timer fires again, it is reset to a MIN(4*T1, T2). This
   process continues so that retransmissions occur with an exponentially
   increasing interval that caps at T2. The default value of T2 is 4s,
   and it represents the amount of time a non-INVITE server transaction
   will take to respond to a request, if it does not respond
   immediately. For the default values of T1 and T2, this results in
   intervals of 500 ms, 1 s, 2 s, 4 s, 4 s, 4 s, etc.

   If Timer F fires while the client transaction is still in the
   "Trying" state, the client transaction SHOULD inform the TU about the
   timeout, and then it SHOULD enter the "Terminated" state. If a
   provisional response is received while in the "Trying" state, the
   response MUST be passed to the TU, and then the client transaction
   SHOULD move to the "Proceeding" state. If a final response (status
   codes 200-699) is received while in the "Trying" state, the response
   MUST be passed to the TU, and the client transaction MUST transition
   to the "Completed" state.

   If Timer E fires while in the "Proceeding" state, the request MUST be
   passed to the transport layer for retransmission, and Timer E MUST be
   reset with a value of T2 seconds. If timer F fires while in the
   "Proceeding" state, the TU MUST be informed of a timeout, and the
   client transaction MUST transition to the terminated state. If a
   final response (status codes 200-699) is received while in the
   "Proceeding" state, the response MUST be passed to the TU, and the
   client transaction MUST transition to the "Completed" state.

   Once the client transaction enters the "Completed" state, it MUST set
   Timer K to fire in T4 seconds for unreliable transports, and zero
   seconds for reliable transports. The "Completed" state exists to
   buffer any additional response retransmissions that may be received
   (which is why the client transaction remains there only for

Rosenberg, et. al. Standards Track [Page 131]

RFC 3261 SIP: Session Initiation Protocol June 2002

   unreliable transports). T4 represents the amount of time the network
   will take to clear messages between client and server transactions.
   The default value of T4 is 5s. A response is a retransmission when
   it matches the same transaction, using the rules specified in Section
   17.1.3. If Timer K fires while in this state, the client transaction
   MUST transition to the "Terminated" state.

   Once the transaction is in the terminated state, it MUST be destroyed
   immediately.

17.1.3 Matching Responses to Client Transactions

   When the transport layer in the client receives a response, it has to
   determine which client transaction will handle the response, so that
   the processing of Sections 17.1.1 and 17.1.2 can take place. The
   branch parameter in the top Via header field is used for this
   purpose. A response matches a client transaction under two
   conditions:

      1. If the response has the same value of the branch parameter in
        the top Via header field as the branch parameter in the top
        Via header field of the request that created the transaction.

      2. If the method parameter in the CSeq header field matches the
        method of the request that created the transaction. The
        method is needed since a CANCEL request constitutes a
        different transaction, but shares the same value of the branch
        parameter.

   If a request is sent via multicast, it is possible that it will
   generate multiple responses from different servers. These responses
   will all have the same branch parameter in the topmost Via, but vary
   in the To tag. The first response received, based on the rules
   above, will be used, and others will be viewed as retransmissions.
   That is not an error; multicast SIP provides only a rudimentary
   "single-hop-discovery-like" service that is limited to processing a
   single response. See Section 18.1.1 for details.

Rosenberg, et. al. Standards Track [Page 132]

RFC 3261 SIP: Session Initiation Protocol June 2002

17.1.4 Handling Transport Errors

        |Request from TU
        |send request
        Timer E V
        send request +-----------+
        +---------| |-------------------+
        | | Trying | Timer F |
        +-------->| | or Transport Err.|
        +-----------+ inform TU |
        200-699 | | |
        resp. to TU | |1xx |
        +---------------+ |resp. to TU |
        | | |
        | Timer E V Timer F |
        | send req +-----------+ or Transport Err. |
        | +---------| | inform TU |
        | | |Proceeding |------------------>|
        | +-------->| |-----+ |
        | +-----------+ |1xx |
        | | ^ |resp to TU |
        | 200-699 | +--------+ |
        | resp. to TU | |
        | | |
        | V |
        | +-----------+ |
        | | | |
        | | Completed | |
        | | | |
        | +-----------+ |
        | ^ | |
        | | | Timer K |
        +--------------+ | - |
        | |
        V |
        NOTE: +-----------+ |
        | | |
        transitions | Terminated|<------------------+
        labeled with | |
        the event +-----------+
        over the action
        to take

        Figure 6: non-INVITE client transaction

   When the client transaction sends a request to the transport layer to
   be sent, the following procedures are followed if the transport layer
   indicates a failure.

Rosenberg, et. al. Standards Track [Page 133]

RFC 3261 SIP: Session Initiation Protocol June 2002

   The client transaction SHOULD inform the TU that a transport failure
   has occurred, and the client transaction SHOULD transition directly
   to the "Terminated" state. The TU will handle the failover
   mechanisms described in [4].

17.2 Server Transaction

   The server transaction is responsible for the delivery of requests to
   the TU and the reliable transmission of responses. It accomplishes
   this through a state machine. Server transactions are created by the
   core when a request is received, and transaction handling is desired
   for that request (this is not always the case).

   As with the client transactions, the state machine depends on whether
   the received request is an INVITE request.

17.2.1 INVITE Server Transaction

   The state diagram for the INVITE server transaction is shown in
   Figure 7.

   When a server transaction is constructed for a request, it enters the
   "Proceeding" state. The server transaction MUST generate a 100
   (Trying) response unless it knows that the TU will generate a
   provisional or final response within 200 ms, in which case it MAY
   generate a 100 (Trying) response. This provisional response is
   needed to quench request retransmissions rapidly in order to avoid
   network congestion. The 100 (Trying) response is constructed
   according to the procedures in Section 8.2.6, except that the
   insertion of tags in the To header field of the response (when none
   was present in the request) is downgraded from MAY to SHOULD NOT.
   The request MUST be passed to the TU.

   The TU passes any number of provisional responses to the server
   transaction. So long as the server transaction is in the
   "Proceeding" state, each of these MUST be passed to the transport
   layer for transmission. They are not sent reliably by the
   transaction layer (they are not retransmitted by it) and do not cause
   a change in the state of the server transaction. If a request
   retransmission is received while in the "Proceeding" state, the most
   recent provisional response that was received from the TU MUST be
   passed to the transport layer for retransmission. A request is a
   retransmission if it matches the same server transaction based on the
   rules of Section 17.2.3.

   If, while in the "Proceeding" state, the TU passes a 2xx response to
   the server transaction, the server transaction MUST pass this
   response to the transport layer for transmission. It is not

Rosenberg, et. al. Standards Track [Page 134]

RFC 3261 SIP: Session Initiation Protocol June 2002

   retransmitted by the server transaction; retransmissions of 2xx
   responses are handled by the TU. The server transaction MUST then
   transition to the "Terminated" state.

   While in the "Proceeding" state, if the TU passes a response with
   status code from 300 to 699 to the server transaction, the response
   MUST be passed to the transport layer for transmission, and the state
   machine MUST enter the "Completed" state. For unreliable transports,
   timer G is set to fire in T1 seconds, and is not set to fire for
   reliable transports.

      This is a change from RFC 2543, where responses were always
      retransmitted, even over reliable transports.

   When the "Completed" state is entered, timer H MUST be set to fire in
   64*T1 seconds for all transports. Timer H determines when the server
   transaction abandons retransmitting the response. Its value is
   chosen to equal Timer B, the amount of time a client transaction will
   continue to retry sending a request. If timer G fires, the response
   is passed to the transport layer once more for retransmission, and
   timer G is set to fire in MIN(2*T1, T2) seconds. From then on, when
   timer G fires, the response is passed to the transport again for
   transmission, and timer G is reset with a value that doubles, unless
   that value exceeds T2, in which case it is reset with the value of
   T2. This is identical to the retransmit behavior for requests in the
   "Trying" state of the non-INVITE client transaction. Furthermore,
   while in the "Completed" state, if a request retransmission is
   received, the server SHOULD pass the response to the transport for
   retransmission.

   If an ACK is received while the server transaction is in the
   "Completed" state, the server transaction MUST transition to the
   "Confirmed" state. As Timer G is ignored in this state, any
   retransmissions of the response will cease.

   If timer H fires while in the "Completed" state, it implies that the
   ACK was never received. In this case, the server transaction MUST
   transition to the "Terminated" state, and MUST indicate to the TU
   that a transaction failure has occurred.

Rosenberg, et. al. Standards Track [Page 135]

RFC 3261 SIP: Session Initiation Protocol June 2002

        |INVITE
        |pass INV to TU
        INVITE V send 100 if TU won't in 200ms
        send response+-----------+
        +--------| |--------+101-199 from TU
        | | Proceeding| |send response
        +------->| |<-------+
        | | Transport Err.
        | | Inform TU
        | |--------------->+
        +-----------+ |
        300-699 from TU | |2xx from TU |
        send response | |send response |
        | +------------------>+
        | |
        INVITE V Timer G fires |
        send response+-----------+ send response |
        +--------| |--------+ |
        | | Completed | | |
        +------->| |<-------+ |
        +-----------+ |
        | | |
        ACK | | |
        - | +------------------>+
        | Timer H fires |
        V or Transport Err.|
        +-----------+ Inform TU |
        | | |
        | Confirmed | |
        | | |
        +-----------+ |
        | |
        |Timer I fires |
        |- |
        | |
        V |
        +-----------+ |
        | | |
        | Terminated|<---------------+
        | |
        +-----------+

        Figure 7: INVITE server transaction

Rosenberg, et. al. Standards Track [Page 136]

RFC 3261 SIP: Session Initiation Protocol June 2002

   The purpose of the "Confirmed" state is to absorb any additional ACK
   messages that arrive, triggered from retransmissions of the final
   response. When this state is entered, timer I is set to fire in T4
   seconds for unreliable transports, and zero seconds for reliable
   transports. Once timer I fires, the server MUST transition to the
   "Terminated" state.

   Once the transaction is in the "Terminated" state, it MUST be
   destroyed immediately. As with client transactions, this is needed
   to ensure reliability of the 2xx responses to INVITE.

17.2.2 Non-INVITE Server Transaction

   The state machine for the non-INVITE server transaction is shown in
   Figure 8.

   The state machine is initialized in the "Trying" state and is passed
   a request other than INVITE or ACK when initialized. This request is
   passed up to the TU. Once in the "Trying" state, any further request
   retransmissions are discarded. A request is a retransmission if it
   matches the same server transaction, using the rules specified in
   Section 17.2.3.

   While in the "Trying" state, if the TU passes a provisional response
   to the server transaction, the server transaction MUST enter the
   "Proceeding" state. The response MUST be passed to the transport
   layer for transmission. Any further provisional responses that are
   received from the TU while in the "Proceeding" state MUST be passed
   to the transport layer for transmission. If a retransmission of the
   request is received while in the "Proceeding" state, the most
   recently sent provisional response MUST be passed to the transport
   layer for retransmission. If the TU passes a final response (status
   codes 200-699) to the server while in the "Proceeding" state, the
   transaction MUST enter the "Completed" state, and the response MUST
   be passed to the transport layer for transmission.

   When the server transaction enters the "Completed" state, it MUST set
   Timer J to fire in 64*T1 seconds for unreliable transports, and zero
   seconds for reliable transports. While in the "Completed" state, the
   server transaction MUST pass the final response to the transport
   layer for retransmission whenever a retransmission of the request is
   received. Any other final responses passed by the TU to the server
   transaction MUST be discarded while in the "Completed" state. The
   server transaction remains in this state until Timer J fires, at
   which point it MUST transition to the "Terminated" state.

   The server transaction MUST be destroyed the instant it enters the
   "Terminated" state.

Rosenberg, et. al. Standards Track [Page 137]

RFC 3261 SIP: Session Initiation Protocol June 2002

17.2.3 Matching Requests to Server Transactions

   When a request is received from the network by the server, it has to
   be matched to an existing transaction. This is accomplished in the
   following manner.

   The branch parameter in the topmost Via header field of the request
   is examined. If it is present and begins with the magic cookie
   "z9hG4bK", the request was generated by a client transaction
   compliant to this specification. Therefore, the branch parameter
   will be unique across all transactions sent by that client. The
   request matches a transaction if:

      1. the branch parameter in the request is equal to the one in the
        top Via header field of the request that created the
        transaction, and

      2. the sent-by value in the top Via of the request is equal to the
        one in the request that created the transaction, and

      3. the method of the request matches the one that created the
        transaction, except for ACK, where the method of the request
        that created the transaction is INVITE.

   This matching rule applies to both INVITE and non-INVITE transactions
   alike.

      The sent-by value is used as part of the matching process because
      there could be accidental or malicious duplication of branch
      parameters from different clients.

   If the branch parameter in the top Via header field is not present,
   or does not contain the magic cookie, the following procedures are
   used. These exist to handle backwards compatibility with RFC 2543
   compliant implementations.

   The INVITE request matches a transaction if the Request-URI, To tag,
   From tag, Call-ID, CSeq, and top Via header field match those of the
   INVITE request which created the transaction. In this case, the
   INVITE is a retransmission of the original one that created the
   transaction. The ACK request matches a transaction if the Request-
   URI, From tag, Call-ID, CSeq number (not the method), and top Via
   header field match those of the INVITE request which created the
   transaction, and the To tag of the ACK matches the To tag of the
   response sent by the server transaction. Matching is done based on
   the matching rules defined for each of those header fields.
   Inclusion of the tag in the To header field in the ACK matching
   process helps disambiguate ACK for 2xx from ACK for other responses

Rosenberg, et. al. Standards Track [Page 138]

RFC 3261 SIP: Session Initiation Protocol June 2002

   at a proxy, which may have forwarded both responses (This can occur
   in unusual conditions. Specifically, when a proxy forked a request,
   and then crashes, the responses may be delivered to another proxy,
   which might end up forwarding multiple responses upstream). An ACK
   request that matches an INVITE transaction matched by a previous ACK
   is considered a retransmission of that previous ACK.

Rosenberg, et. al. Standards Track [Page 139]

RFC 3261 SIP: Session Initiation Protocol June 2002

        |Request received
        |pass to TU
        V
        +-----------+
        | |
        | Trying |-------------+
        | | |
        +-----------+ |200-699 from TU
        | |send response
        |1xx from TU |
        |send response |
        | |
        Request V 1xx from TU |
        send response+-----------+send response|
        +--------| |--------+ |
        | | Proceeding| | |
        +------->| |<-------+ |
        +<--------------| | |
        |Trnsprt Err +-----------+ |
        |Inform TU | |
        | | |
        | |200-699 from TU |
        | |send response |
        | Request V |
        | send response+-----------+ |
        | +--------| | |
        | | | Completed |<------------+
        | +------->| |
        +<--------------| |
        |Trnsprt Err +-----------+
        |Inform TU |
        | |Timer J fires
        | |-
        | |
        | V
        | +-----------+
        | | |
        +-------------->| Terminated|
        | |
        +-----------+

        Figure 8: non-INVITE server transaction

   For all other request methods, a request is matched to a transaction
   if the Request-URI, To tag, From tag, Call-ID, CSeq (including the
   method), and top Via header field match those of the request that
   created the transaction. Matching is done based on the matching

Rosenberg, et. al. Standards Track [Page 140]

RFC 3261 SIP: Session Initiation Protocol June 2002

   rules defined for each of those header fields. When a non-INVITE
   request matches an existing transaction, it is a retransmission of
   the request that created that transaction.

   Because the matching rules include the Request-URI, the server cannot
   match a response to a transaction. When the TU passes a response to
   the server transaction, it must pass it to the specific server
   transaction for which the response is targeted.

17.2.4 Handling Transport Errors

   When the server transaction sends a response to the transport layer
   to be sent, the following procedures are followed if the transport
   layer indicates a failure.

   First, the procedures in [4] are followed, which attempt to deliver
   the response to a backup. If those should all fail, based on the
   definition of failure in [4], the server transaction SHOULD inform
   the TU that a failure has occurred, and SHOULD transition to the
   terminated state.

3.7. Notifier Generation of NOTIFY Requests

   Notifications are generated for the dialog package when an INVITE
   request is sent, when a new dialog comes into existence at a UA, or
   when the state or characteristics of an existing dialog changes.
   Therefore, a model of dialog state is needed in order to determine
   precisely when to send notifications, and what their content should
   be. The SIP specification has a reasonably well defined lifecycle
   for dialogs. However, it is not explicitly modelled. This
   specification provides an explicit model of dialog state through a
   finite state machine.

   It is RECOMMENDED that NOTIFY requests only contain information on
   the dialogs whose state or participation information has changed.
   However, if a notifier receives a SUBSCRIBE request, the triggered
   NOTIFY SHOULD contain the state of all dialogs that the subscriber is
   authorized to see.

3.7.1. The Dialog State Machine

   Modelling of dialog state is complicated by two factors. The first
   is forking, which can cause a single INVITE to generate many dialogs
   at a UAC. The second is the differing views of state at the UAC
   (user agent client) and UAS (usage agent server). We have chosen to
   handle the first issue by extending the dialog finite state machine
   (FSM) to include the states between transmission of the INVITE and
   the creation of actual dialogs through receipt of 1xx and 2xx
   responses. As a result, this specification supports the notion of
   dialog state for dialogs before they are fully instantiated.

   We have also chosen to use a single FSM for both UAC and UAS.

Rosenberg, et al. Standards Track [Page 8]

RFC 4235 Dialog Package November 2005

        +----------+ +----------+
        | | 1xx-notag | |
        | |----------->| |
        | Trying | |Proceeding|-----+
        | |---+ +-----| | |
        | | | | | | |
        +----------+ | | +----------+ |
        | | | | | |
        | | | | | |
        +<--C-----C--+ |1xx-tag |
        | | | | |
        cancelled| | | V |
        rejected| | |1xx-tag +----------+ |
        | | +------->| | |2xx
        | | | | |
        +<--C--------------| Early |-----C---+ 1xx-tag
        | | replaced | | | | w/new tag
        | | | |<----C---+ (new FSM
        | | +----------+ | instance
        | | 2xx | | created)
        | +----------------+ | |
        | | |2xx |
        | | | |
        V V V |
        +----------+ +----------+ |
        | | | | |
        | | | | |
        |Terminated|<-----------| Confirmed|<----+
        | | error | |
        | | timeout | |
        +----------+ replaced +----------+
        local-bye | ^
        remote-bye | |
        | |
        +------+
        2xx w. new tag
        (new FSM instance
        created)

        Figure 3

   The FSM for dialog state is shown in Figure 3. The FSM is best
   understood by considering the UAC and UAS cases separately.

Rosenberg, et al. Standards Track [Page 9]

RFC 4235 Dialog Package November 2005

   The FSM is created in the Trying state when the UAC sends an INVITE
   request. Upon receipt of a 1xx without a tag, the FSM transitions to
   the Proceeding state. Note that there is no actual dialog yet, as
   defined by the SIP specification. However, there is a "half-dialog",
   in the sense that two of the three components of the dialog ID (the
   call identifier and local tag) are known. If a 1xx with a tag is
   received, the FSM transitions to the Early state. The full dialog
   identifier is now defined. Had a 2xx been received, the FSM would
   have transitioned to the Confirmed state.

   If, after transitioning to the Early or Confirmed states, the UAC
   receives another 1xx or 2xx respectively with a different tag,
   another instance of the FSM is created, initialized into the Early or
   Confirmed state, respectively. The benefit of this approach is that
   there will be a single FSM representing the entire state of the
   invitation and resulting dialog when dealing in the common case of no
   forking.

   If the UAC sends a CANCEL and then subsequently receives a 487 to its
   INVITE transaction, all FSMs spawned from that INVITE transition to
   the Terminated state with the event "cancelled". If the UAC receives
   a new invitation (with a Replaces [13] header) that replaces the
   current Early or Confirmed dialog, all INVITE transactions spawned
   from the replaced invitation transition to the Terminated state with
   the event "replaced". If the INVITE transaction terminates with a
   non-2xx response for any other reason, all FSMs spawned from that
   INVITE transition to the Terminated state with the event "rejected".

   Once in the Confirmed state, the call is active. It can transition
   to the Terminated state if the UAC sends a BYE or receives a BYE
   (corresponding to the "local-bye" and "remote-bye" events as
   appropriate), if a mid-dialog request generates a 481 or 408 response
   (corresponding to the "error" event), or a mid-dialog request
   generates no response (corresponding to the "timeout" event).

   From the perspective of the UAS, when an INVITE is received, the FSM
   is created in the Trying state. If it sends a 1xx without a tag, the
   FSM transitions to the Proceeding state. If a 1xx is sent with a
   tag, the FSM transitions to the Early state, and if a 2xx is sent, it
   transitions to the Confirmed state. If the UAS receives a CANCEL
   request and then generates a 487 response to the INVITE (which can
   occur in the Proceeding and Early states), the FSM transitions to the
   Terminated state with the event "cancelled". If the UAS generates
   any other non-2xx final response to the INVITE request, the FSM
   transitions to the Terminated state with the event "rejected". If
   the UAS receives a new invitation (with a Replaces [13] header field)
   that replaces the current Confirmed dialog, the replaced invitation
   transitions to the Terminated state with the event "replaced". Once

Rosenberg, et al. Standards Track [Page 10]

RFC 4235 Dialog Package November 2005

   in the Confirmed state, the other transitions to the Terminated state
   occur for the same reasons they do in the case of UAC.

      There should never be a transition from the Trying state to the
      Terminated state with the event "cancelled", since the SIP
      specification prohibits transmission of CANCEL until a provisional
      response is received. However, this transition is defined in the
      FSM just to unify the transitions from Trying, Proceeding, and
      Early states to the Terminated state.

3.7.2. Applying the State Machine

   The notifier MAY generate a NOTIFY request on any event transition of
   the FSM. Whether it does or not is policy dependent. However, some
   general guidelines are provided.

   When the subscriber is unauthenticated, or it is authenticated but
   represents a third party with no specific authorization policies, it
   is RECOMMENDED that subscriptions to an individual dialog or to a
   specific set of dialogs be forbidden. Only subscriptions to all
   dialogs (i.e., there are no dialog identifiers in the Event header
   field) are permitted. In that case, actual dialog states across all
   dialogs will not be reported. Rather, a single "virtual" dialog FSM
   will be used, and event transitions on that FSM will be reported.

   If there is any dialog at the UA whose state is Confirmed, the
   virtual FSM is in the Confirmed state. If there are no dialogs at
   the UA in the Confirmed state but there is at least one in the Early
   state, the virtual FSM is in the Early or Confirmed state. If there
   are no dialogs in the Confirmed or Early states but there is at least
   one in the Proceeding state, the virtual FSM is in the Proceeding,
   Early, or Confirmed state. If there are no dialogs in the Confirmed,
   Early, or Proceeding states but there is at least one in the Trying
   state, the virtual FSM is in the Trying, Proceeding, Early or
   Confirmed state. The choice of state to use depends on whether the
   UA wishes to let unknown users know that their phone is ringing, as
   opposed to being in an active call.

   It is RECOMMENDED that, in the absence of any preference, Confirmed
   is used in all cases as shown in the example in Section 3.6.
   Furthermore, it is RECOMMENDED that the notifications of changes in
   the virtual FSM machine not convey any information except the state
   of the FSM and its event transitions - no dialog identifiers (which
   are ill-defined in this model in any case). The use of this virtual
   FSM allows minimal information to be conveyed. A subscriber cannot
   know how many calls are in progress, or with whom, just that there
   exists a call. This is the same information they would receive if

Rosenberg, et al. Standards Track [Page 11]

RFC 4235 Dialog Package November 2005

   they simply sent an INVITE to the user instead; a 486 (Busy Here)
   response would indicate that they are on a call.

   When the subscriber is authenticated and has authenticated itself
   with the same address-of-record that the UA itself uses, if no
   explicit authorization policy is defined, it is RECOMMENDED that all
   state transitions on dialogs that have been subscribed to be
   reported, along with complete dialog IDs. This means either all of
   the dialogs, if no dialog identifiers were present in the Event
   header field, or the specific set of dialogs identified by the Event
   header field parameters.

   The notifier SHOULD generate a NOTIFY request on any change in the
   characteristics associated with the dialog. Since these include
   Contact URIs, Contact parameters, and session descriptions, receipt
   of re-INVITEs and UPDATE requests [3] that modify this information
   MAY trigger notifications.

3.8. Subscriber Processing of NOTIFY Requests

   The SIP Events framework expects packages to specify how a subscriber
   processes NOTIFY requests in package-specific ways. In particular, a
   package should specify how it uses the NOTIFY requests to construct a
   coherent view of the state of the subscribed resource.

   Typically, the NOTIFY for the dialog package will contain information
   about only those dialogs whose state has changed. To construct a
   coherent view of the total state of all dialogs, a subscriber to the
   dialog package will need to combine NOTIFYs received over time.

   Notifications within this package can convey partial information;
   that is, they can indicate information about a subset of the state
   associated with the subscription. This means that an explicit
   algorithm needs to be defined in order to construct coherent and
   consistent state. The details of this mechanism are specific to the
   particular document type. See Section 4.3 for information on
   constructing coherent information from an application/dialog-info+xml
   document.

3.9. Handling of Forked Requests

   Since dialog state is distributed across the UA for a particular
   user, it is reasonable and useful for a SUBSCRIBE request for dialog
   state to fork and to reach multiple UAs.

   As a result, a forked SUBSCRIBE request for dialog state can install
   multiple subscriptions. Subscribers to this package MUST be prepared

Rosenberg, et al. Standards Track [Page 12]

RFC 4235 Dialog Package November 2005

   to install subscription state for each NOTIFY generated as a result
   of a single SUBSCRIBE.

3.10. Rate of Notifications

   For reasons of congestion control, it is important that the rate of
   notifications not be excessive. It is RECOMMENDED that the server
   not generate notifications for a single subscriber faster than once
   every 1 second.

3.11. State Agents

   Dialog state is ideally maintained in the user agents in which the
   dialog resides. Therefore, the elements that maintain the dialog are
   the ones best suited to handle subscriptions to it. However, in some
   cases, a network agent may also know the state of the dialogs held by
   a user. Such state agents MAY be used with this package.

4. Dialog Information Format

   Dialog information is an XML document [4] that MUST be well-formed
   and SHOULD be valid. Dialog information documents MUST be based on
   XML 1.0 and MUST be encoded using UTF-8. This specification makes
   use of XML namespaces for identifying dialog information documents
   and document fragments. The namespace URI for elements defined by
   this specification is a URN [5], using the namespace identifier
   'ietf' defined by [6] and extended by [7]. This URN is:

      urn:ietf:params:xml:ns:dialog-info

   A dialog information document begins with the root element tag
   "dialog-info".

4.1. Structure of Dialog Information

   A dialog information document starts with a dialog-info element.
   This element has three mandatory attributes:
   o version: This attribute allows the recipient of dialog information
      documents to properly order them. Versions start at 0, and
      increment by one for each new document sent to a subscriber.
      Versions are scoped within a subscription. Versions MUST be
      representable using a non-negative 32 bit integer.
   o state: This attribute indicates whether the document contains the
      full dialog information, or whether it contains only information
      on those dialogs that have changed since the previous document
      (partial).
Rosenberg, et al. Standards Track [Page 13]

RFC 4235 Dialog Package November 2005

   o entity: This attribute contains a URI that identifies the user
      whose dialog information is reported in the remainder of the
      document. This user is referred to as the "observed user".

   The dialog-info element has a series of zero or more dialog sub-
   elements. Each of those represents a specific dialog. An example:

      <?xml version="1.0"?>
      <dialog-info xmlns="urn:ietf:params:xml:ns:dialog-info"
        version="0" notify-state="full"
        entity="sip:alice@example.com">
      </dialog-info>

4.1.1. Dialog Element

   The dialog element reports information about a specific dialog or
   "half-dialog". It has a single mandatory attribute: id. The id
   attribute provides a single string that can be used as an identifier
   for this dialog or "half-dialog". This is a different identifier
   than the dialog ID defined in RFC 3261 [2], but related to it.

   For a caller, the id is created when an INVITE request is sent. When
   a 1xx response with a tag, or a 2xx response is received, the dialog
   is formally created. The id remains unchanged. However, if an
   additional 1xx or 2xx is received, resulting in the creation of
   another dialog (and resulting FSM), that dialog is allocated a new
   id.

   For a callee, the id is created when an INVITE outside of an existing
   dialog is received. When a 2xx or a 1xx with a tag is sent, creating
   the dialog, the id remains unchanged.

   The id MUST be unique amongst all current dialogs at a UA.

   There are a number of optional attributes that provide identification
   information about the dialog:

      o call-id: This attribute is a string that represents the call-id
        component of the dialog identifier. (Note that single and
        double quotes inside a call-id must be escaped using &quote;
        for " and &apos; for ' .)

      o local-tag: This attribute is a string that represents the
        local-tag component of the dialog identifier.

      o remote-tag: This attribute is a string that represents the
        remote-tag component of the dialog identifier. The remote tag
        attribute won't be present if there is only a "half-dialog",

Rosenberg, et al. Standards Track [Page 14]

RFC 4235 Dialog Package November 2005

        resulting from the generation of an INVITE for which no final
        responses or provisional responses with tags has been received.

      o direction: This attribute is either initiator or recipient, and
        indicates whether the observed user was the initiator of the
        dialog, or the recipient of the INVITE that created it.

      <?xml version="1.0"?>
      <dialog-info xmlns="urn:ietf:params:xml:ns:dialog-info"
        version="0" state="partial"
        entity="sip:alice@example.com">
        <dialog id="as7d900as8" call-id="a84b4c76e66710"
        local-tag="1928301774" direction="initiator">
      ...
        </dialog>
      </dialog-info>

   The sub-elements of the dialog element provide additional information
   about the dialog. Some of these sub-elements provide more detail
   about the dialog itself, while the local and remote sub-elements
   describe characteristics of the participants involved in the dialog.
   The only mandatory sub-element is the state element.

4.1.2. State Element

   The "state" element indicates the state of the dialog. Its value is
   an enumerated type describing one of the states in the FSM above. It
   has an optional event attribute that can be used to indicate the
   event that caused any transition into the terminated state, and an
   optional code attribute that indicates the response code associated
   with any transition caused by a response to the original INVITE.

      <state event="rejected" code="486">terminated</state>

4.1.3. Duration Element

   The "duration" element contains the amount of time, in seconds, since
   the FSM was created.

      <duration>145</duration>

4.1.4. Replaces Element

   The "replaces" element is used to correlate a new dialog with one it
   replaced as a result of an invitation with a Replaces header field.
   This element is present in the replacement dialog only (the newer
   dialog) and contains attributes with the call-id, local-tag, and
   remote-tag of the replaced dialog.
Rosenberg, et al. Standards Track [Page 15]

RFC 4235 Dialog Package November 2005

      <replaces call-id="hg287s98s89"
        local-tag="6762h7" remote-tag="09278hsb"/>

4.1.5. Referred-By Element

   The "referred-by" element is used to correlate a new dialog with a
   REFER [12] request that triggered it. The element is present in a
   dialog that was triggered by a REFER request that contained a
   Referred-By [11] header field and contains the (optional) display
   name attribute and the Referred-By URI as its value.

      <referred-by display="Bob">sip:bob@example.com</referred-by>

4.1.6. Local and Remote Elements

   The "local" and "remote" elements are sub-elements of the dialog
   element that contain information about the local and remote
   participants, respectively. They both have a number of optional
   sub-elements that indicate the identity conveyed by the participant,
   the target URI, the feature-tags of the target, and the
   session-description of the participant.

4.1.6.1. Identity Element

   The "identity" element indicates a local or remote URI, as defined in
   [2] as appropriate. It has an optional attribute, display, that
   contains the display name from the appropriate URI.

      Note that multiple identities (for example a sip: URI and a tel:
      URI) could be included if they all correspond to the participant.
      To avoid repeating identity information in each request, the
      subscriber can assume that the identity URIs are the same as in
      previous notifications if no identity elements are present in the
      corresponding local or remote element. If any identity elements
      are present in the local or remote part of a notification, the new
      list of identity tags completely supersedes the old list in the
      corresponding part.

      <identity display="Anonymous">
        sip:anonymous@anonymous.invalid</identity>

4.1.6.2. Target Element

   The "target" contains the local or remote target URI constructed by
   the user agent for this dialog, as defined in RFC 3261 [2] in a "uri"
   attribute.
Rosenberg, et al. Standards Track [Page 16]

RFC 4235 Dialog Package November 2005

   It can contain a list of Contact header parameters in param sub-
   elements (such as those defined in [10]). The param element contains
   two required attributes, pname and pval. Boolean parameters are
   represented by the explicit pval values, "true" and "false" (for
   example, when a feature parameter is explicitly negated). Parameters
   that have no value at all are represented by the explicit pval value
   "true". The param element itself has no contents. To avoid
   repeating Contact information in each request, the subscriber can
   assume that the target URI and parameters are the same as in previous
   notifications if no target element is present in the corresponding
   local or remote element. If a target element is present in the local
   or remote part of a notification, the new target tag and list of
   parameter tags completely supersedes the old target and parameter
   list in the corresponding part. Note that any quoting (including
   extra angle-bracket quoting used to quote string values in [10]) or
   backslash escaping MUST be removed before being placed in a pval
   attribute. Any remaining single quotes, double quotes, and
   ampersands MUST be properly XML escaped.

      <target uri="sip:alice@pc33.example.com">
        <param pname="isfocus" pval="true"/>
        <param pname="class" pval="business"/>
        <param pname="description" pval="Alice's desk &amp; office"/>
        <param pname="sip.rendering" pval="no"/>
      </target>

4.1.6.3. Session Description Element

   The session-description element contains the session description used
   by the observed user for its end of the dialog. This element should
   generally NOT be included in the notifications, unless it was
   explicitly requested by the subscriber. It has a single attribute,
   "type", which indicates the MIME media type of the session
   description. To avoid repeating session description information in
   each request, the subscriber can assume that the session description
   is the same as in previous notifications if no session description
   element is present in the corresponding local or remote element.